## Slide 1: ENGI 301 “Stupidly Secure Safe” Proposal
October 22nd, 2019
John Perez

## Slide 2: Background Information
The proposed project would effectively be a safe with three levels of security
The safe would be closed with three solenoid locks, each wired to a different unlock mechanism
  The three mechanisms represent unique ways to open a lock – keypad, pattern lock, and dial combination lock
When one of the three mechanisms is correctly activated (i.e. the correct password input, the correct pattern put in, or correct number combination) and enter button pressed, the associated lock would disengage, and a green indicator light would turn on
  An incorrect password results in a red indicator light to flash
With all three correct passwords put in and all three locks disengaged, the door will be able to physically open
The user can access the contents, close the door, then press a reset button to turn off green indicator lights and relock all three locks simultaneously

## Slide 3: Background Information
ENTER
ENTER
ENTER
1
2
3
1
2
3
RESET

## Slide 4: Background Information
ENTER
ENTER
ENTER
1
2
3
Correct
Indicator Lights
Incorrect
Indicator Lights
Door w/ Solenoid Locks
Keypad
Pattern Lock w/ buttons
Combination Lock w/ dials
1
2
3
RESET
Reset Button

## Slide 5: Notes on Design
Physical System
  Beyond electronic hardware components, tools in the OEDK could be used to create the safe itself
  The box, door, and handle are all physical systems that could be manufactured in the OEDK
  While the safe would ideally be made of metal, laser cut wood can be used for prototyping
  Button covers can be made at the OEDK as well using 3D printers or similar

## Slide 6: Addendum: Advanced Design
To better take advantage of the PocketBeagle a more advanced security system will be put in place
  A 2 factor identification system will be used so the user texts themselves a secure password
  That password is then entered into the keypad

## Slide 7: Notes on Design
Areas for potential change
  Instead of 3 separate solenoid locks, 1 could be used. This single lock would require activation from all 3 password inputs to disengage
  Enter buttons could be removed in favor of an automatic entry of password
  The dial combo section could be reduced to a single dial for simplicity – this would still have an adequate security value

## Slide 8: Background Information
Preexisting projects
  Timed lockbox using an Arduino: https://www.hackster.io/LoganSpace42/arduino-lock-box-0d52c0
  Pattern lock: https://www.hackster.io/najad/pattern-lock-8ede38
  Keypad lock: https://www.hackster.io/camdelk/keypad-entry-lock-4d7a03

## Slide 9: System Block Diagram
Create a System Block Diagram
  Label interfaces / pins
  Components (part numbers if possible)

## Slide 10: System Block Diagram
Keypad
Button 1
Button 2
Button 3
Dial 1
Dial 2
Dial 3
Red LED 1
Red LED 2
Red LED 3
G. LED 1
G. LED 2
G. LED 3
Solenoid 1
Solenoid 2
Solenoid 3
RESET Button
Enter Button
Enter Button
Enter Button
GPIO 109
GPIO 59
GPIO 58
GPIO 57

## Slide 11: System Block Diagram
Keypad
Button 1
Button 2
Button 3
Dial 1
Dial 2
Dial 3
Red LED 1
Red LED 2
Red LED 3
G. LED 1
G. LED 2
G. LED 3
Solenoid
Enter Button
Enter Button
AIN
GPIO
GPIO
GPIO
Enter Button
GPIO
Send Button
Note: These are all different GPIO channels

## Slide 12: Power Block Diagram
Red LED 1
Red LED 2
Red LED 3
G. LED 1
G. LED 2
G. LED 3
USB Connection
VIN_BAT
SYS_OUT
Solenoid 1
12 V Battery
USB Power

## Slide 13: Components / Budget
Component | Need to Buy | Cost (total)
Keypad | x1 | 5.95
Button (Pattern, Enter, Reset) | x3, x3, x1 | 2.50
Turn Potentiometer (Dial) | x3 | 3.75
Green LED | x3 | 1.08
Red LED | x3 | 1.80
Linear Solenoid (Lock) | x3 | 44.85

## Slide 14: Components
Link to Components w/ specific names
  4x4 Matrix Keypad: https://www.adafruit.com/product/3844
  Tactile Button Switch: https://www.adafruit.com/product/367
  Potentiometer with built-in in knob: https://www.adafruit.com/product/4133
  Lock-Style Solenoid: https://www.adafruit.com/product/1512
  Green 569nm LED Indication: https://www.digikey.com/product-detail/en/lite-on-inc/LTL-4233/160-1130-ND/217580
    OEDK
  Red 630nm LED Indication: https://www.digikey.com/product-detail/en/rohm-semiconductor/SLR-56VR3F/511-1264-ND/636992
    OEDK